## Slide 1: Chapter 5
Image pre-processing
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 2: Image pre-processing
Pixel brightness transformations
Geometric transformations
Local pre-processing
  Image smoothing, edge detection, line detection, corner detection, and region detection.
Image restoration
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 3: Edge detectors
Edge detectors are a collection of very important local image pre-processing methods used to locate changes in the intensity function.
Edges are pixels where the intensity function (brightness) changes abruptly.
If only edge elements with strong magnitude are considered, such information often suffices (足夠) for image understanding.
For example, line drawing images.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
http://kelpie77.deviantart.com/art/line-art-horse-123352124

## Slide 4: Edge detectors
Physical phenomena (現象) in the image formation process lead to abrupt changes in image values
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 5: Edge detectors
An edge is a property attached to an individual pixel and is calculated from the image function behavior in a neighborhood of that pixel.
It is a vector variable with two components.
  Magnitude
    The edge magnitude is the magnitude of the gradient.
  Direction
    The edge direction is rotated with respect to the gradient direction by .
    The gradient direction gives the direction of maximum growth of the function.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 6: Edge detectors
Edges are often used in image analysis for finding region boundaries.
This figure shows examples of several standard edge profile (輪廓、外形).
Edge detectors are usually tuned for some type of edge profile.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 7: Edge detectors
The gradient magnitude and gradient direction are continuous image functions calculated as
where is the angle (in radians;弳度) from the axis to .
Laplacian operator: (obtained only edge magnitudes without orientations)
  The Laplacian has the same properties in all directions and is therefore invariant to rotation.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 8: Edge detectors
Image sharpening has the objective of making edges steeper.
  The sharpened output image is obtained from the input image as
  where is positive coefficient which gives the strength of sharpening
  is a measure of the image function sheerness (陡峭)
  For example, image sharpening using a Laplacian
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
Original image

## Slide 9: Edge detectors
The derivatives (導數) can be approximated by differences in digital images.
  The first differences of the image in the vertical direction (for fixed ) and in the horizontal direction (for fixed ) are
  where is a small integer, usually 1.
  Symmetric expressions for the differences
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 10: Edge detectors
Robert operator [1965]
  It uses only a neighborhood of the current pixel.
  The magnitude of the edge is computed as
  Disadvantage:
    Its high sensitivity to noise: very few pixels are used to approximate the gradient.

## Slide 11: Edge detectors
Laplace operator
  The Laplace operator is a very popular operator approximating the second derivative which gives the edge magnitude only.
  A mask is often used. For 4-neighborhoods and 8-neighborhoods it is defined as
  A Laplacian operator with stressed significance of the central pixel or its neighborhood is sometimes used.
  Disadvantage: It responds doubly to some edges in the image.

## Slide 12: Edge detectors
Prewitt operator
  The Prewitt operator approximates the first derivative.
  The gradient is estimated in eight (for a convolution mask) possible directions, and the convolution result of greatest magnitude indicates the gradient direction.
  Some examples of masks
  Larger marks are possible, for example, or .
  PS. The direction of the gradient is given by the mask giving maximal response. This is also the case for all the following operator approximating the first derivative.

## Slide 13: Edge detectors
First-derivative edge detection using Prewitt operators.
  North direction
    The brighter the pixel value, the stronger the edge.
  East direction
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
North
East
Strong edges

## Slide 14: Edge detectors
Sobel operator
  The Sobel operator approximates the first derivative.
  Some examples of masks
  The Sobel operator is often used as a simple detector of horizontality () and verticality of edges.
    If the response is and the response , we might then derive edge magnitude as and direction as of edges.

## Slide 15: Edge detectors
Kirsch operator
  The Kirsch operator approximates the first derivative.
  Some examples of masks
  The direction of the gradient is given by the mask giving maximal response.

## Slide 16: Zero-crossings of the second derivative
Zero-crossings
  An edge detection technique using the second derivative.
  The first derivative of the image function should have an extremum at the position corresponding to the image.
  The second derivative should be zero at the same position.
  However, it is much easier and more precise to find a zero-crossing position than an extremum.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 17: Zero-crossings of the second derivative
Zero-crossings
  How to compute the second derivative robustly?
    To smooth an image first (to reduce noise)
    The 2D Gaussian smoothing operator (a Gaussian filter) is given by
  where : the image co-ordinates
  : a standard deviation
    Sometimes this is presented with a normalizing factor
  and
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 18: Zero-crossings of the second derivative
Zero-crossings
  Our goal is to obtain a second derivative of a smoothed 2D function .
  Laplacian of Gaussian (LoG)
  where : Laplace operator
  : convolution operator
  Because of the linearity of the operators
  The derivative of the Gaussian filter can be pre-computed.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 19: Zero-crossings of the second derivative
The derivative of the Gaussian filter
The convolution mask of a LoG
where normalizes the sum of mask elements to zero. (!!)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 20: Zero-crossings of the second derivative
The convolution mask of a LoG
The inverted LoG operator is commonly called a Mexican hat.
  For example, a discrete approximation is
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 22: Zero-crossings of the second derivative
LoG v.s. DoG
  The operator can be very effectively approximated by convolution with a mask that is the difference of two Gaussian averaging masks with substantially different .
  The method is called the difference of Gaussians (DoG)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
Comparison of difference of Gaussian with Mexican hat wavelet
https://en.wikipedia.org/wiki/Difference_of_Gaussians
DoG
Mexican
hat

## Slide 23
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
Original image
A post-processing step to avoid detection of zero-crossings corresponding to non-significant edges in regions of almost constant gray-level will admit only those zero-crossings for which there is sufficient edge evidence from a first-derivative edge detector.
DoG
Zero-crossings of DoG
LoG zc
DoG zc

## Slide 24: Scale in image processing
Different description levels are easily interpreted as different scales in the domain of digital images.
  to eliminate fine scale noise
  to separate events at different scales
Scale-independent description of object can reduce the ambiguity.
Three examples of the application of multiple scale description
  To find the curve segments that represents the underlying structure of the scene needs to be found.
    For example, the figure may be interpreted as a closed curve, or be described as two intersecting straight lines.
  Scale-space filtering
  Canny edge detector
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 25: Scale in image processing
Scale-space filtering
  Try to describe signals qualitatively (在質的方面) with respect to scale
  The original 1D signal is smoothed by convolution with a 1D Gaussian
  If the standard deviation is slowly changed, the function
  represents a surface on the plane that is called the scale-space image.
  Inflexion points (反曲點) of the curve for a distinct value
  describe the curve qualitatively (對質的描述).
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 26: Scale-space filtering
Andrew P. Witkin.
Fai'rchi'ld Laboratory for Artiﬁcial Intelligence Research

## Slide 27
An example of 2D scale-space representation
Larger scale t (or ): fewer noises, less precise in location
Smaller scale t (or ): more noises, more precise in location
https://en.wikipedia.org/wiki/Scale_space

## Slide 28: Canny edge detection
Canny edge detection
  It is optimal for step edges corrupted by white noise.
  The optimality of the detector is related to three criteria.
    The detection criterion
      The important edges should not be missed.
      There should be no spurious (假的) edges.
    The localization criterion
      The distance between the actual and located position of the edge should be minimal.
    The one response criterion
      Minimizing multiple responses to a single edge
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 29: Canny edge detection
Suppose is a 2D Gaussian and assume we wish to convolve the image with an operator which is a first derivative of in some direction
  We would like is perpendicular (垂直) to the edge: this direction is not known in advance. (: Sobel operator or Prewitt operators)
To estimate : If is the image, the normal () to the edge is
The edge location is then at the local maximum of the image convolved with the operator in the direction (zero-crossing)
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 30: Canny edge detection
Substituting in equation (5.56) for from equation (5.54)
  This equation illustrates how to find local maxima in the direction perpendicular to the edge (non-maximal suppression—Algorithm 6.4)
    Non-maximal suppression is an edge thinning technique.
The magnitude of the edge is measured as
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 31: Non-maximal Suppression
Non-maximal suppression is an edge thinning technique.
After applying gradient calculation, the edge extracted from the gradient value is still quite blurred. Non-maximal suppression can help to suppress all the gradient values (by setting them to 0) except the local maxima, which indicate locations with the sharpest change of intensity value.
http://ccy.dd.ncu.edu.tw/~chen/course/vision/ch6/%E5%96%AE%E5%85%83%E5%85%AD%E3%80%81%E9%82%8A%E7%B7%A3%E5%81%B5%E6%B8%AC.pdf

## Slide 32: Canny edge detection
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
Algorithm 5.4 Canny edge detection
1. Convolve an image with a Gaussian of scale .
2. Estimate local edge normal directions using equation
for each pixel in the image.
3. Find the location of the edges using . (non-maximal suppression)
4. Compute the magnitude of the edge using .
5. Threshold edges in the image with hysteresis (滯後作用) (Algorithm 6.5) to eliminate spurious (假的) responses.
6. Repeat steps (1) through (5) for ascending values of the standard deviation .
7. Aggregate the final information about edges at multiple scale using the ‘feature synthesis(合成)’ approach.
https://en.wikipedia.org/wiki/Canny_edge_detector

## Slide 33: Hysteresis Thresholding
Double threshold: Select high and low threshold values
  If an edge pixel’s gradient value is higher than the high threshold value, it is marked as a strong edge pixel.
  If an edge pixel’s gradient value is smaller than the high threshold value and larger than the low threshold value, it is marked as a weak edge pixel.
  If an edge pixel's value is smaller than the low threshold value, it will be suppressed.
Edge tracking by hysteresis (滯後作用)
  Usually a weak edge pixel caused from true edges will be connected to a strong edge pixel while noise responses are unconnected.
  To track the edge connection, blob analysis is applied by looking at a weak edge pixel and its 8-connected neighborhood pixels.
  As long as there is one strong edge pixel that is involved in the blob, that weak edge point can be identified as one that should be preserved.
https://en.wikipedia.org/wiki/Canny_edge_detector

## Slide 34: Canny edge detection
Some examples
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 35
http://www.codeproject.com/Articles/93642/Canny-Edge-Detection-in-C

## Slide 36: Canny edge detection
https://www.mathworks.com/examples/image/mw/images-ex48835658-detect-edges-in-images

## Slide 37: Parametric edge models
Parametric models are based on the idea that the discrete image intensity function can be considered a sampled and noisy approximation of an underlying continuous or piecewise continuous image intensity function.
Piecewise (分段地) continuous function estimates called facets (小平面) are used to represent (a neighborhood of) each image pixel.
  Such an image representation is called a facet model.
  For example, linear, quadratic, and bi-cubic facet models.
  An example of a bi-cubic facet model
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
https://stackoverflow.com/questions/30433391/how-can-i-produce-multi-point-linear-interpolation/30438865#30438865

## Slide 38: Parametric edge models
Once the facet model parameters are available for each image pixel, edges can be detected as extrema of the first directional derivative and/or zero-crossings of the second directional derivative of the local continuous facet model functions.
Edge detectors based on parametric models describe edges more precisely than convolution-based edge detectors.
  They carry the potential for subpixel edge localization.
  However, their computational requirements are much higher.
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle
http://cs.joensuu.fi/~koles/approximation/Ch3_5.html

## Slide 39: Edges in multi-spectral images
One pixel in a multi-spectral image is described by an -dimensional vector, and brightness values in spectral bands are the vector components.
There are several possibilities for the detection of edges in multi-spectral images.
  Detect edges separately in individual image spectral components
  Create a multi-spectral edge detector which uses brightness information from all spectral bands
Image Processing, Analysis, and Machine Vision, 4th Edition Sonka, Hlavac & Boyle

## Slide 40
http://patingtoci24.soup.io/post/390611507/Download-multispectral-imaging
http://www.agricultureuavs.com/photos_multispectral_camera.htm